## Slide 1: UART PROTOCOL DESIGN AND VERIFICATION
Team -13

## Slide 2: Introduction
What is UART?
UART (Universal Asynchronous Receiver-Transmitter) is a widely used communication protocol for serial data transfer.
It allows full-duplex communication between two devices without requiring a clock signal.
Data is transmitted as a sequence of bits with start, stop, and optional parity bits for error detection.
Why Verification is Important?
Ensures that the UART design behaves correctly under different scenarios.
Detects protocol violations, timing issues, and data corruption.
Verification significantly reduces debugging time during silicon bring-up.

## Slide 3: Why use a UART?
A UART may be used when High speed is not required
An inexpensive communication link between two devices is required
UART communication is very cheap
Single wire for each direction (plus ground wire)
Asynchronous because no clock signal is transmitted
Relatively simple hardware
PC devices such as mice and modems used to often use UARTs for communication to the PC

## Slide 4: Overview of the UART Module
Transmit (TX) Side: Converts parallel data into a serial stream, handles start/stop bits, and controls baud rate.
Receive (RX) Side: Converts received serial data into parallel format and detects errors.
Baud Rate Generator: Configures transmission speed to match the receiving device.
Key Features of the UART DUT
Configurable baud rate, stop bits, parity.
FIFO buffer to store transmitted and received data.
Error detection for frame errors, parity errors, and overflow.

## Slide 5: UVM Testbench Components
Transaction (Sequence Item): Defines the data structure used for stimulus generation.
Generator (Sequence): Generates stimulus based on constraints.
Driver: Converts transaction data into interface signals for DUT.
Monitor: Captures and records transactions from the DUT.
Scoreboard: Compares actual and expected results.
Coverage: Tracks whether all functional aspects are exercised.

## Slide 6: UART Functions
Transmitter
Convert from parallel to serial
Add start and stop delineators (bits)
Add parity bit
Receiver
Convert from serial to parallel
Remove start and stop delineators (bits)
Check and remove parity bit

## Slide 7: UART Character Transmission
Uses a single wire for transmission
Each bit has a fixed time duration determined by the transmission rate
Example a 1200 bps (bits per second) UART will have a 1/1200 s or about 833.3 µs bit duration
The start bit marks the beginning of a new word
When detected, the receiver synchronizes with the new data stream
Next follows the data bits (7 or 8)
The least significant bit is sent first

## Slide 8: Contd…
The parity bit is added to make the number of 1s even (even parity) or odd (odd parity)
This bit can be used by the receiver to check for transmission errors
Use of parity bits is optional.
The stop bit marks the end of transmission
Receiver checks to make sure it is 1
Separates one word from the start bit of the next word
In the configuration shown, it takes 10 bits to send 7 bits of data
Transmission efficiency is 7/10, or 70

## Slide 9: UART Character Reception
Start bit says a character is coming, receiver resets its timers Receiver should sample in middle of bits.
Receiver uses a timer (counter) to time when it samples. Transmission rate (i.e., bit duration) must be known.
Receiver also verifies that stop bit is 1,If not, reports framing error to host system
New start bit can appear immediately after stop bit,Receiver will resynchronize on each start bit

## Slide 10: UART Options
usually have programmable options
Data 7 or 8 bits
Parity even, odd, none, mark, space
Stop bits 1, 1.5, 2
Baud rate 300, 1200, 2400, 4800, 9600, 19.2k, 38.4k, 57.6k, 115.2k
The symbol rate of the transmission system
For a UART, same as the number of bits per second (bps)
Each bit is 1/(rate) seconds wide
Example
9600 baud ? 9600 Hz
9600 bits per second (bps)
Each bit is 1/(9600 Hz) 104.17 µs long